Baseline Summary B1173 (FREN to BIGW)

| Processed: | Friday, Apr 02, 2004 06:52:59AM |
| --- | --- |
| Solution type: | Iono free fixed |
| Solution acceptability: | Solution acceptable |
| Ephemeris used: | Precise |
| Met Data: | Standard |
| Baseline slope distance: | 12459.148m |
| Elevation mask: | 15 degrees |
| Variance ratio: | 46.1 |
| Reference variance: | 0.380 |
| RMS: | 0.007m |
| Horizontal Precision 1-sigma (scaled): | 0.001m |
| Vertical Precision 1-sigma (scaled): | 0.001m |

| Start time (GPS Time): | 04/03/18, 17:58:30.000 | 1262, 410310.000 |
| --- | --- | --- |
| Stop time (GPS Time): | 04/03/18, 18:45:15.000 | 1262, 413115.000 |
| Occupation time: | 00:46:45.000 |

Baseline Components (Mark to Mark)

| From: | FREN |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 712695.841m | Latitude | 39°34'56.81840"N | Latitude | 39°34'56.81839"N |
| Easting | 1978548.658m | Longitude | 122°14'58.92998"W | Longitude | 122°14'58.92998"W |
| Elevation | 50.607m | Height | 21.664m | Height | 21.664m |

| To: | BIGW |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 722724.305m | Latitude | 39°40'21.22428"N | Latitude | 39°40'21.22428"N |
| Easting | 1971157.006m | Longitude | 122°20'10.23324"W | Longitude | 122°20'10.23324"W |
| Elevation | 140.157m | Height | 111.175m | Height | 111.175m |

| Baseline: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 10028.465m | NS Fwd Azimuth | 323°27'01" |  X | -2903.674m |
|  Easting | -7391.652m | Ell. Distance | 12458.698m |  Y | 9302.341m |
|  Elevation | 89.550m |  Height | 89.511m |  Z | 7763.085m |

Standard Errors

| Baseline Errors: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 0.001m |  NS Fwd Azimuth | 0.017 seconds |  X | 0.001m |
|  Easting | 0.001m |  Ell.Distance | 0.001m |  Y | 0.002m |
|  Elevation | 0.002m |  Height | 0.002m |  Z | 0.002m |

Aposteriori Covariance Matrix

|  | X | Y | Z |
| --- | --- | --- | --- |
| X | 1.042e-6m2 |  |  |
| Y | 8.315e-7m2 | 3.596e-6m2 |  |
| Z | -4.607e-7m2 | -2.151e-6m2 | 2.318e-6m2 |

Occupations

|  | From | To |
| --- | --- | --- |
| Point Name: | FREN | BIGW |
| Data file: | FREN0782.DAT | BIGW0782.DAT |
| Receiver Type: | 4000SSi | 4000SSi |
| Receiver Serial Number: | 17633 | 14632 |
| Antenna type: | Permanent L1/L2 | Compact L1/L2 w/Ground Plane |
| Measured To: | Bottom of antenna mount | Antenna Phase Center |
| Antenna height | Measured | 2.000m | 1.952m |
|  | APC | 2.067m | 1.952m |

Tracking Summary

Residuals

Processing Style - Precise Ephemeris

| Elevation Mask | 15 degrees |
| --- | --- |
| Ephemeris | Precise |
| Solution Type | Fixed |

Static

| Minimum baseline observation time | 120 seconds |
| --- | --- |
| Maximum baseline length to attempt a fixed solution : |
| Using broadcast ephemeris | 200 kilometers |
| Using precise ephemeris | 2000 kilometers |

Kinematic

| Minimum reference observation time | 600 seconds |
| --- | --- |
| Minimum static initialization observation time | 120 seconds |
| Minimum known point initialization ratio | 3.000 |
| Minimum OTF processing time | 200 seconds |

Global

| Frequency type | L1 |
| --- | --- |
| Maximum fixable cycle slip (static processing only) | 600 seconds |
| Maximum iterations (static processing only) | 10 |
| Maximum integer search time (static processing only) | 30 minutes |
| Antenna Model | NGS |

Quality

|  | Single frequency | Dual frequency |
| --- | --- | --- |
|  | Flag | Fail | Flag | Fail |
| RMS acceptance criteria | 0.030 | 0.040 | 0.020 | 0.030 |
| Ratio acceptance criteria | 3.000 | 1.500 | 3.000 | 1.500 |
| Reference variance acceptance criteria | 10.000 | 20.000 | 5.000 | 10.000 |
| Edit multiplier | 3.500 |

Tropo

| Model | Hopfield |
| --- | --- |
| Minimum zenith delay interval | 2 hours |
| Use observed met data | Enabled |

Iono

| Ambiguity resolution pass (static processing only) | Enabled |
| --- | --- |
| Apply to all baselines longer than | 10 kilometers |
| Final pass | Enabled |
| Apply to all baselines longer than | 5 kilometers |

Events

| Interpolation method | Linear |
| --- | --- |
| Number of points to fit | 2 |
| Maximum allowed missing epochs | 0 |
| Time offset | 0 microseconds |

OTF Search

| Search method | Optimal |
| --- | --- |