Baseline Summary B1311 (A107 to WINS)

| Processed: | Friday, Apr 02, 2004 06:52:59AM |
| --- | --- |
| Solution type: | Iono free fixed |
| Solution acceptability: | Solution acceptable |
| Ephemeris used: | Precise |
| Met Data: | Standard |
| Baseline slope distance: | 13519.279m |
| Elevation mask: | 15 degrees |
| Variance ratio: | 75.2 |
| Reference variance: | 0.788 |
| RMS: | 0.010m |
| Horizontal Precision 1-sigma (scaled): | 0.001m |
| Vertical Precision 1-sigma (scaled): | 0.003m |

| Start time (GPS Time): | 04/03/19, 19:44:45.000 | 1262, 503085.000 |
| --- | --- | --- |
| Stop time (GPS Time): | 04/03/19, 20:43:45.000 | 1262, 506625.000 |
| Occupation time: | 00:59:00.000 |

Baseline Components (Mark to Mark)

| From: | A107 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 713100.284m | Latitude | 39°35'08.37555"N | Latitude | 39°35'08.37554"N |
| Easting | 1965214.377m | Longitude | 122°24'17.77975"W | Longitude | 122°24'17.77975"W |
| Elevation | 151.675m | Height | 122.540m | Height | 122.540m |

| To: | WINS |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 721798.949m | Latitude | 39°39'48.71406"N | Latitude | 39°39'48.71405"N |
| Easting | 1954866.506m | Longitude | 122°31'33.53477"W | Longitude | 122°31'33.53477"W |
| Elevation | 200.643m | Height | 171.657m | Height | 171.656m |

| Baseline: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 8698.664m | NS Fwd Azimuth | 309°47'47" |  X | -5829.081m |
|  Easting | -10347.870m | Ell. Distance | 13518.881m |  Y | 10199.246m |
|  Elevation | 48.968m |  Height | 49.116m |  Z | 6690.897m |

Standard Errors

| Baseline Errors: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 0.001m |  NS Fwd Azimuth | 0.011 seconds |  X | 0.001m |
|  Easting | 0.001m |  Ell.Distance | 0.001m |  Y | 0.003m |
|  Elevation | 0.003m |  Height | 0.003m |  Z | 0.002m |

Aposteriori Covariance Matrix

|  | X | Y | Z |
| --- | --- | --- | --- |
| X | 1.786e-6m2 |  |  |
| Y | 2.880e-6m2 | 8.793e-6m2 |  |
| Z | -1.978e-6m2 | -3.988e-6m2 | 3.390e-6m2 |

Occupations

|  | From | To |
| --- | --- | --- |
| Point Name: | A107 | WINS |
| Data file: | A1070793.DAT | WINS0793.DAT |
| Receiver Type: | 4000SSi | 4000SSi |
| Receiver Serial Number: | 7613 | 14594 |
| Antenna type: | Compact L1/L2 w/Ground Plane | Compact L1/L2 w/Ground Plane |
| Measured To: | Antenna Phase Center | Antenna Phase Center |
| Antenna height | Measured | 2.063m | 1.952m |
|  | APC | 2.063m | 1.952m |

Tracking Summary

Residuals

Processing Style - Precise Ephemeris

| Elevation Mask | 15 degrees |
| --- | --- |
| Ephemeris | Precise |
| Solution Type | Fixed |

Static

| Minimum baseline observation time | 120 seconds |
| --- | --- |
| Maximum baseline length to attempt a fixed solution : |
| Using broadcast ephemeris | 200 kilometers |
| Using precise ephemeris | 2000 kilometers |

Kinematic

| Minimum reference observation time | 600 seconds |
| --- | --- |
| Minimum static initialization observation time | 120 seconds |
| Minimum known point initialization ratio | 3.000 |
| Minimum OTF processing time | 200 seconds |

Global

| Frequency type | L1 |
| --- | --- |
| Maximum fixable cycle slip (static processing only) | 600 seconds |
| Maximum iterations (static processing only) | 10 |
| Maximum integer search time (static processing only) | 30 minutes |
| Antenna Model | NGS |

Quality

|  | Single frequency | Dual frequency |
| --- | --- | --- |
|  | Flag | Fail | Flag | Fail |
| RMS acceptance criteria | 0.030 | 0.040 | 0.020 | 0.030 |
| Ratio acceptance criteria | 3.000 | 1.500 | 3.000 | 1.500 |
| Reference variance acceptance criteria | 10.000 | 20.000 | 5.000 | 10.000 |
| Edit multiplier | 3.500 |

Tropo

| Model | Hopfield |
| --- | --- |
| Minimum zenith delay interval | 2 hours |
| Use observed met data | Enabled |

Iono

| Ambiguity resolution pass (static processing only) | Enabled |
| --- | --- |
| Apply to all baselines longer than | 10 kilometers |
| Final pass | Enabled |
| Apply to all baselines longer than | 5 kilometers |

Events

| Interpolation method | Linear |
| --- | --- |
| Number of points to fit | 2 |
| Maximum allowed missing epochs | 0 |
| Time offset | 0 microseconds |

OTF Search

| Search method | Optimal |
| --- | --- |