Baseline Summary B1339 (ARTO to L191)

| Processed: | Saturday, Mar 20, 2004 07:45:45PM |
| --- | --- |
| Solution type: | Iono free fixed |
| Solution acceptability: | Solution acceptable |
| Ephemeris used: | Precise |
| Met Data: | Standard |
| Baseline slope distance: | 8495.203m |
| Elevation mask: | 10 degrees |
| Variance ratio: | 19.1 |
| Reference variance: | 0.392 |
| RMS: | 0.007m |
| Horizontal Precision 1-sigma (scaled): | 0.002m |
| Vertical Precision 1-sigma (scaled): | 0.004m |

| Start time (GPS Time): | 04/03/19, 21:43:45.000 | 1262, 510225.000 |
| --- | --- | --- |
| Stop time (GPS Time): | 04/03/19, 22:30:15.000 | 1262, 513015.000 |
| Occupation time: | 00:46:30.000 |

Baseline Components (Mark to Mark)

| From: | ARTO |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 717334.758m | Latitude | 39°37'27.55350"N | Latitude | 39°37'27.55349"N |
| Easting | 1982423.387m | Longitude | 122°12'16.99590"W | Longitude | 122°12'16.99590"W |
| Elevation | 57.089m | Height | 28.356m | Height | 28.356m |

| To: | L191 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 712627.066m | Latitude | 39°34'55.31470"N | Latitude | 39°34'55.31470"N |
| Easting | 1989494.383m | Longitude | 122°07'20.24049"W | Longitude | 122°07'20.24049"W |
| Elevation | 39.933m | Height | 11.377m | Height | 11.377m |

| Baseline: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | -4707.692m | NS Fwd Azimuth | 123°31'31" |  X | 4406.937m |
|  Easting | 7070.995m | Ell. Distance | 8495.161m |  Y | -6291.453m |
|  Elevation | -17.157m |  Height | -16.979m |  Z | -3628.361m |

Standard Errors

| Baseline Errors: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 0.004m |  NS Fwd Azimuth | 0.078 seconds |  X | 0.001m |
|  Easting | 0.001m |  Ell.Distance | 0.002m |  Y | 0.002m |
|  Elevation | 0.006m |  Height | 0.006m |  Z | 0.007m |

Aposteriori Covariance Matrix

|  | X | Y | Z |
| --- | --- | --- | --- |
| X | 2.074e-6m2 |  |  |
| Y | 2.419e-6m2 | 3.975e-6m2 |  |
| Z | -7.411e-6m2 | -1.063e-5m2 | 4.325e-5m2 |

Occupations

|  | From | To |
| --- | --- | --- |
| Point Name: | ARTO | L191 |
| Data file: | ARTO0794.DAT | L1910794.DAT |
| Receiver Type: | 4000SSi | 4000SSi |
| Receiver Serial Number: | 7618 | 6782 |
| Antenna type: | Compact L1/L2 w/Ground Plane | Compact L1/L2 w/Ground Plane |
| Measured To: | Antenna Phase Center | Antenna Phase Center |
| Antenna height | Measured | 2.063m | 2.063m |
|  | APC | 2.063m | 2.063m |

Tracking Summary

Residuals

Processing Style - Precise Ephemeris 10° Mask

| Elevation Mask | 10 degrees |
| --- | --- |
| Ephemeris | Precise |
| Solution Type | Fixed |

Static

| Minimum baseline observation time | 120 seconds |
| --- | --- |
| Maximum baseline length to attempt a fixed solution : |
| Using broadcast ephemeris | 200 kilometers |
| Using precise ephemeris | 2000 kilometers |

Kinematic

| Minimum reference observation time | 600 seconds |
| --- | --- |
| Minimum static initialization observation time | 120 seconds |
| Minimum known point initialization ratio | 3.000 |
| Minimum OTF processing time | 200 seconds |

Global

| Frequency type | L1 |
| --- | --- |
| Maximum fixable cycle slip (static processing only) | 600 seconds |
| Maximum iterations (static processing only) | 10 |
| Maximum integer search time (static processing only) | 30 minutes |
| Antenna Model | NGS |

Quality

|  | Single frequency | Dual frequency |
| --- | --- | --- |
|  | Flag | Fail | Flag | Fail |
| RMS acceptance criteria | 0.030 | 0.040 | 0.020 | 0.030 |
| Ratio acceptance criteria | 3.000 | 1.500 | 3.000 | 1.500 |
| Reference variance acceptance criteria | 10.000 | 20.000 | 5.000 | 10.000 |
| Edit multiplier | 3.500 |

Tropo

| Model | Hopfield |
| --- | --- |
| Minimum zenith delay interval | 2 hours |
| Use observed met data | Enabled |

Iono

| Ambiguity resolution pass (static processing only) | Enabled |
| --- | --- |
| Apply to all baselines longer than | 10 kilometers |
| Final pass | Enabled |
| Apply to all baselines longer than | 5 kilometers |

Events

| Interpolation method | Linear |
| --- | --- |
| Number of points to fit | 2 |
| Maximum allowed missing epochs | 0 |
| Time offset | 0 microseconds |

OTF Search

| Search method | Optimal |
| --- | --- |