Baseline Summary B1466 (A107 to B107)

| Processed: | Friday, Apr 02, 2004 06:52:59AM |
| --- | --- |
| Solution type: | Iono free fixed |
| Solution acceptability: | Solution acceptable |
| Ephemeris used: | Precise |
| Met Data: | Standard |
| Baseline slope distance: | 10998.970m |
| Elevation mask: | 15 degrees |
| Variance ratio: | 70.3 |
| Reference variance: | 0.322 |
| RMS: | 0.006m |
| Horizontal Precision 1-sigma (scaled): | 0.000m |
| Vertical Precision 1-sigma (scaled): | 0.001m |

| Start time (GPS Time): | 04/03/22, 16:19:45.000 | 1263, 145185.000 |
| --- | --- | --- |
| Stop time (GPS Time): | 04/03/22, 17:30:30.000 | 1263, 149430.000 |
| Occupation time: | 01:10:45.000 |

Baseline Components (Mark to Mark)

| From: | A107 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 713100.276m | Latitude | 39°35'08.37528"N | Latitude | 39°35'08.37528"N |
| Easting | 1965214.377m | Longitude | 122°24'17.77974"W | Longitude | 122°24'17.77974"W |
| Elevation | 151.686m | Height | 122.551m | Height | 122.551m |

| To: | B107 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 716010.708m | Latitude | 39°36'40.98145"N | Latitude | 39°36'40.98145"N |
| Easting | 1954608.444m | Longitude | 122°31'42.94882"W | Longitude | 122°31'42.94882"W |
| Elevation | 216.063m | Height | 187.074m | Height | 187.073m |

| Baseline: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 2910.432m | NS Fwd Azimuth | 285°05'25" |  X | -8010.796m |
|  Easting | -10605.933m | Ell. Distance | 10998.516m |  Y | 7195.735m |
|  Elevation | 64.377m |  Height | 64.523m |  Z | 2241.851m |

Standard Errors

| Baseline Errors: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 0.001m |  NS Fwd Azimuth | 0.009 seconds |  X | 0.001m |
|  Easting | 0.001m |  Ell.Distance | 0.001m |  Y | 0.001m |
|  Elevation | 0.001m |  Height | 0.001m |  Z | 0.001m |

Aposteriori Covariance Matrix

|  | X | Y | Z |
| --- | --- | --- | --- |
| X | 4.734e-7m2 |  |  |
| Y | 2.780e-7m2 | 7.614e-7m2 |  |
| Z | -3.763e-7m2 | -4.637e-7m2 | 7.757e-7m2 |

Occupations

|  | From | To |
| --- | --- | --- |
| Point Name: | A107 | B107 |
| Data file: | A1070821.DAT | B1070821.DAT |
| Receiver Type: | 4000SSE | 4000SSi |
| Receiver Serial Number: | 1547 | 14631 |
| Antenna type: | Compact L1/L2 w/Ground Plane | Compact L1/L2 w/Ground Plane |
| Measured To: | Antenna Phase Center | Antenna Phase Center |
| Antenna height | Measured | 2.063m | 2.063m |
|  | APC | 2.063m | 2.063m |

Tracking Summary

Residuals

Processing Style - Precise Ephemeris

| Elevation Mask | 15 degrees |
| --- | --- |
| Ephemeris | Precise |
| Solution Type | Fixed |

Static

| Minimum baseline observation time | 120 seconds |
| --- | --- |
| Maximum baseline length to attempt a fixed solution : |
| Using broadcast ephemeris | 200 kilometers |
| Using precise ephemeris | 2000 kilometers |

Kinematic

| Minimum reference observation time | 600 seconds |
| --- | --- |
| Minimum static initialization observation time | 120 seconds |
| Minimum known point initialization ratio | 3.000 |
| Minimum OTF processing time | 200 seconds |

Global

| Frequency type | L1 |
| --- | --- |
| Maximum fixable cycle slip (static processing only) | 600 seconds |
| Maximum iterations (static processing only) | 10 |
| Maximum integer search time (static processing only) | 30 minutes |
| Antenna Model | NGS |

Quality

|  | Single frequency | Dual frequency |
| --- | --- | --- |
|  | Flag | Fail | Flag | Fail |
| RMS acceptance criteria | 0.030 | 0.040 | 0.020 | 0.030 |
| Ratio acceptance criteria | 3.000 | 1.500 | 3.000 | 1.500 |
| Reference variance acceptance criteria | 10.000 | 20.000 | 5.000 | 10.000 |
| Edit multiplier | 3.500 |

Tropo

| Model | Hopfield |
| --- | --- |
| Minimum zenith delay interval | 2 hours |
| Use observed met data | Enabled |

Iono

| Ambiguity resolution pass (static processing only) | Enabled |
| --- | --- |
| Apply to all baselines longer than | 10 kilometers |
| Final pass | Enabled |
| Apply to all baselines longer than | 5 kilometers |

Events

| Interpolation method | Linear |
| --- | --- |
| Number of points to fit | 2 |
| Maximum allowed missing epochs | 0 |
| Time offset | 0 microseconds |

OTF Search

| Search method | Optimal |
| --- | --- |