Baseline Summary B1570 (J143 to B107)

| Processed: | Tuesday, May 25, 2004 07:01:20AM |
| --- | --- |
| Solution type: | Iono free fixed |
| Solution acceptability: | Solution acceptable |
| Ephemeris used: | Precise |
| Met Data: | Standard |
| Baseline slope distance: | 72703.197m |
| Elevation mask: | 15 degrees |
| Variance ratio: | 4.8 |
| Reference variance: | 1.575 |
| RMS: | 0.015m |
| Horizontal Precision 1-sigma (scaled): | 0.001m |
| Vertical Precision 1-sigma (scaled): | 0.005m |

| Start time (GPS Time): | 04/03/22, 19:59:15.000 | 1263, 158355.000 |
| --- | --- | --- |
| Stop time (GPS Time): | 04/03/23, 01:00:15.000 | 1263, 176415.000 |
| Occupation time: | 05:01:00.000 |

Baseline Components (Mark to Mark)

| From: | J143 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 716465.204m | Latitude | 39°36'58.45013"N | Latitude | 39°36'58.45012"N |
| Easting | 2027307.409m | Longitude | 121°40'55.11741"W | Longitude | 121°40'55.11741"W |
| Elevation | 63.706m | Height | 36.176m | Height | 36.176m |

| To: | B107 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 716008.143m | Latitude | 39°36'40.89853"N | Latitude | 39°36'40.89853"N |
| Easting | 1954609.788m | Longitude | 122°31'42.89184"W | Longitude | 122°31'42.89184"W |
| Elevation | 216.434m | Height | 187.445m | Height | 187.445m |

| Baseline: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | -457.061m | NS Fwd Azimuth | 269°50'36" |  X | -61828.437m |
|  Easting | -72697.621m | Ell. Distance | 72702.160m |  Y | 38247.829m |
|  Elevation | 152.728m |  Height | 151.269m |  Z | -320.558m |

Standard Errors

| Baseline Errors: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 0.001m |  NS Fwd Azimuth | 0.002 seconds |  X | 0.002m |
|  Easting | 0.000m |  Ell.Distance | 0.000m |  Y | 0.002m |
|  Elevation | 0.004m |  Height | 0.004m |  Z | 0.002m |

Aposteriori Covariance Matrix

|  | X | Y | Z |
| --- | --- | --- | --- |
| X | 2.582e-6m2 |  |  |
| Y | 3.717e-6m2 | 5.971e-6m2 |  |
| Z | -3.598e-6m2 | -5.462e-6m2 | 5.706e-6m2 |

Occupations

|  | From | To |
| --- | --- | --- |
| Point Name: | J143 | B107 |
| Data file: | J1430822.DAT | B1070820.DAT |
| Receiver Type: | 4000SSi | 4000SSi |
| Receiver Serial Number: | 14594 | 17633 |
| Antenna type: | Compact L1/L2 w/Ground Plane | Compact L1/L2 w/Ground Plane |
| Measured To: | Antenna Phase Center | Antenna Phase Center |
| Antenna height | Measured | 1.952m | 2.063m |
|  | APC | 1.952m | 2.063m |

Tracking Summary

Residuals

Processing Style - Precise Ephemeris

| Elevation Mask | 15 degrees |
| --- | --- |
| Ephemeris | Precise |
| Solution Type | Fixed |

Static

| Minimum baseline observation time | 120 seconds |
| --- | --- |
| Maximum baseline length to attempt a fixed solution : |
| Using broadcast ephemeris | 200 kilometers |
| Using precise ephemeris | 2000 kilometers |

Kinematic

| Minimum reference observation time | 600 seconds |
| --- | --- |
| Minimum static initialization observation time | 120 seconds |
| Minimum known point initialization ratio | 3.000 |
| Minimum OTF processing time | 200 seconds |

Global

| Frequency type | L1 |
| --- | --- |
| Maximum fixable cycle slip (static processing only) | 600 seconds |
| Maximum iterations (static processing only) | 10 |
| Maximum integer search time (static processing only) | 30 minutes |
| Antenna Model | NGS |

Quality

|  | Single frequency | Dual frequency |
| --- | --- | --- |
|  | Flag | Fail | Flag | Fail |
| RMS acceptance criteria | 0.030 | 0.040 | 0.020 | 0.030 |
| Ratio acceptance criteria | 3.000 | 1.500 | 3.000 | 1.500 |
| Reference variance acceptance criteria | 10.000 | 20.000 | 5.000 | 10.000 |
| Edit multiplier | 3.500 |

Tropo

| Model | Hopfield |
| --- | --- |
| Minimum zenith delay interval | 2 hours |
| Use observed met data | Enabled |

Iono

| Ambiguity resolution pass (static processing only) | Enabled |
| --- | --- |
| Apply to all baselines longer than | 10 kilometers |
| Final pass | Enabled |
| Apply to all baselines longer than | 5 kilometers |

Events

| Interpolation method | Linear |
| --- | --- |
| Number of points to fit | 2 |
| Maximum allowed missing epochs | 0 |
| Time offset | 0 microseconds |

OTF Search

| Search method | Optimal |
| --- | --- |