Baseline Summary B774 (HOWA to ADOB)

| Processed: | Friday, Apr 02, 2004 06:52:59AM |
| --- | --- |
| Solution type: | Iono free fixed |
| Solution acceptability: | Solution acceptable |
| Ephemeris used: | Precise |
| Met Data: | Standard |
| Baseline slope distance: | 5558.214m |
| Elevation mask: | 15 degrees |
| Variance ratio: | 37.3 |
| Reference variance: | 0.530 |
| RMS: | 0.008m |
| Horizontal Precision 1-sigma (scaled): | 0.001m |
| Vertical Precision 1-sigma (scaled): | 0.001m |

| Start time (GPS Time): | 04/03/16, 17:42:45.000 | 1262, 236565.000 |
| --- | --- | --- |
| Stop time (GPS Time): | 04/03/16, 18:30:45.000 | 1262, 239445.000 |
| Occupation time: | 00:48:00.000 |

Baseline Components (Mark to Mark)

| From: | HOWA |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 694651.465m | Latitude | 39°25'12.48875"N | Latitude | 39°25'12.48875"N |
| Easting | 2008789.993m | Longitude | 121°53'52.49926"W | Longitude | 121°53'52.49926"W |
| Elevation | 23.415m | Height | -5.090m | Height | -5.090m |

| To: | ADOB |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Grid |  | Local |  | WGS 84 |  |
| Northing | 691387.885m | Latitude | 39°23'26.77967"N | Latitude | 39°23'26.77966"N |
| Easting | 2004291.266m | Longitude | 121°57'00.66122"W | Longitude | 121°57'00.66122"W |
| Elevation | 22.461m | Height | -6.249m | Height | -6.249m |

| Baseline: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | -3263.579m | NS Fwd Azimuth | 234°06'20" |  X | -4914.730m |
|  Easting | -4498.727m | Ell. Distance | 5558.219m |  Y | 624.790m |
|  Elevation | -0.953m |  Height | -1.159m |  Z | -2519.683m |

Standard Errors

| Baseline Errors: |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  Northing | 0.001m |  NS Fwd Azimuth | 0.025 seconds |  X | 0.001m |
|  Easting | 0.001m |  Ell.Distance | 0.001m |  Y | 0.001m |
|  Elevation | 0.002m |  Height | 0.002m |  Z | 0.001m |

Aposteriori Covariance Matrix

|  | X | Y | Z |
| --- | --- | --- | --- |
| X | 8.721e-7m2 |  |  |
| Y | 6.533e-7m2 | 1.372e-6m2 |  |
| Z | -4.356e-7m2 | -6.917e-7m2 | 1.024e-6m2 |

Occupations

|  | From | To |
| --- | --- | --- |
| Point Name: | HOWA | ADOB |
| Data file: | HOWA0762-3.DAT | ADOB0762-3.DAT |
| Receiver Type: | 4000SSE | 4000SSi |
| Receiver Serial Number: | 1547 | 7618 |
| Antenna type: | Compact L1/L2 w/Ground Plane | Compact L1/L2 w/Ground Plane |
| Measured To: | Antenna Phase Center | Antenna Phase Center |
| Antenna height | Measured | 2.063m | 2.063m |
|  | APC | 2.063m | 2.063m |

Tracking Summary

Residuals

Processing Style - Precise Ephemeris

| Elevation Mask | 15 degrees |
| --- | --- |
| Ephemeris | Precise |
| Solution Type | Fixed |

Static

| Minimum baseline observation time | 120 seconds |
| --- | --- |
| Maximum baseline length to attempt a fixed solution : |
| Using broadcast ephemeris | 200 kilometers |
| Using precise ephemeris | 2000 kilometers |

Kinematic

| Minimum reference observation time | 600 seconds |
| --- | --- |
| Minimum static initialization observation time | 120 seconds |
| Minimum known point initialization ratio | 3.000 |
| Minimum OTF processing time | 200 seconds |

Global

| Frequency type | L1 |
| --- | --- |
| Maximum fixable cycle slip (static processing only) | 600 seconds |
| Maximum iterations (static processing only) | 10 |
| Maximum integer search time (static processing only) | 30 minutes |
| Antenna Model | NGS |

Quality

|  | Single frequency | Dual frequency |
| --- | --- | --- |
|  | Flag | Fail | Flag | Fail |
| RMS acceptance criteria | 0.030 | 0.040 | 0.020 | 0.030 |
| Ratio acceptance criteria | 3.000 | 1.500 | 3.000 | 1.500 |
| Reference variance acceptance criteria | 10.000 | 20.000 | 5.000 | 10.000 |
| Edit multiplier | 3.500 |

Tropo

| Model | Hopfield |
| --- | --- |
| Minimum zenith delay interval | 2 hours |
| Use observed met data | Enabled |

Iono

| Ambiguity resolution pass (static processing only) | Enabled |
| --- | --- |
| Apply to all baselines longer than | 10 kilometers |
| Final pass | Enabled |
| Apply to all baselines longer than | 5 kilometers |

Events

| Interpolation method | Linear |
| --- | --- |
| Number of points to fit | 2 |
| Maximum allowed missing epochs | 0 |
| Time offset | 0 microseconds |

OTF Search

| Search method | Optimal |
| --- | --- |